Digital display constant temperature

Digestion Apparatus

The digital display constant temperature digestion instrument can digest and determine the chemical oxygen demand (COD), total phosphorus (TP), total nitrogen (TN), urine and blood samples, hair, etc. in various surface water, domestic water, and industrial wastewater. It is widely used in the identification and management of water quality by environmental protection departments, water resources management departments and public health departments. Digestion principle: Put the sample and digestion fluid in the digestion tube, and perform digestion at a constant temperature, so that the sample is thoroughly digested and used for various instrumental and chemical analysis. Digestion sample range: various water samples, biological samples (blood, urine, hair), cosmetics, etc.

Technical Parameters:

- Temperature control range:RT -300℃

(special note: temperature refers to the temperature of the constant temperature block, the temperature of the digested sample liquid is the same as the boiling point of the digestion liquid).

(2) Temperature stability: ±1℃. Temperature control accuracy: ±0.5℃

(3) Number of digestion holes: ( )holes, diameter: Φ16.5mm, suitable for digestion tubes with an outer diameter of Φ16mm.

(4) Temperature control method: Microcomputer PID control, LED display, clear and intuitive.

(5) Material of heating part: aluminum alloy.